## Slide 1: CSC 373 Winter 2020 Prof. Lytinen
Cache memory

## Slide 2: We’d like cache memory to contain what the CPU is about to interact with But this is difficult to predict. So we’ll estimate by predicting that the CPU will look at the same memory address(es) that it just did. “Principal of locality”

## Slide 3: Locality for instructions Usually, code is running sequentially, or a small piece of code is running iteratively. If we’re lucky, the whole piece can fit in 1 cache block. Locality for data Data items that are being accessed tend to be near each other (arrays and strings are contiguous; local variables for a function are all together, etc.)

## Slide 4: For data… If the CPU wants data that is not in the cache, we have a cache “miss” If the CPU wants data that is in the cache, this is called a cache “hit” We like to maximize the “hit” ratio (and minimize “miss” ratio) … same for instructions

## Slide 5: Cache miss vs. hit
Each cache miss takes ~5x more than a cache hit
Processes access a lot of memory
  Even if data in mainly in registers, there are things like arrays, strings which are in memory
  All instructions are in memory until copied into the IR

## Slide 6: To illustrate caching, we will assume that our computer has registers, 1 type of cache, main memory (RAM), and 1 disk. Again , a low-level process can only place data into a register main memory it has no access to the cache or the disk

## Slide 7: Memory hierarchy: holds for caches, disks, perhaps connected systems. Each faster level of memory lf contains a copy of the data in ls In general, lf has copies of many contiguous subpieces of ls.

## Slide 8: Vocab for caching Sets are equally-divided pieces of the cache. Sets contain one or more lines. When each set contains just one line, this is called direct map caching. When each set contains n lines, this is called set-associative caching. Each line contains a block (although sometimes all 3 terms are used interchangeably).

## Slide 9
Main Memory is also divided into blocks that are the same size as blocks in the cache. Obviously, # blocks in memory >>> # blocks/lines in cache When a memory location is needed and is not in the cache, then the block that it is a member of is copied into a cache set.

## Slide 10: Cache hits and misses
If the current instruction wants data that is stored in the cache, it is called a cache hit.
If the desired data is in main memory or on the disk, it is called a cache miss.
We’d like to maximize the % of cache hits

## Slide 11: Cache hits and misses
Each block of main memory can only be placed in one set. This is determined by the physical address of the start of the block. Specifically, the set bits of the address determine the cache set.
This approach is used so that the cache does not have to be searched in order to find a block of data (which would take time)

## Slide 12: Cache lines
v ttt..tttt dd dd dd … dd dd
v means valid; a single bit which indicates whether or not a set contains data (it might be empty)
t means tag; a marker to indicate which particular block is contained by a line
d means data; the contents of a block

## Slide 13: The whole cache
s0 v ttt..tttt dd dd dd … dd dd
s1 v ttt..tttt dd dd dd … dd dd
s2 v ttt..tttt dd … dd dd dd dd
…
(depends on how many sets)

## Slide 14: Real numbers
On cdmlinux, we can see cache sizes with the lscpu command.
L1d cache: 32K
L1i cache: 32K
L2 cache: 256K
L3 cache: 12288K
cdmlinux doesn’t tell us its block size or the number of sets.

## Slide 15: Fake numbers
Let’s assume
8-bit addressing
1 cache (L1)
cache has 4 sets; therefore 2 set bits
blocks are 16 bytes; therefore 4 offset bits (24 = 16)
Therefore, there must be 2 tag bits (2 + 2 + 4 = 8)

## Slide 16: Ordering of bits in memory addresses
For our 8-bit addressing, ttssoooo (t=tag, s=set, o=offset)
Example: 0xb8
t = 10, s=11, o=1000
Example: 0x27?
t = ?, s=?, o=?

## Slide 17: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0 0
S1 0
S2 0
S3 0
v t data

## Slide 18: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0 0
S1 0
S2 0
S3 0 CACHE MISS – it’s empty
v t data
0xf2 = 11 11 0010 (tag=11, set=11, offset=0010)

## Slide 19: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0 0
S1 0
S2 0
S3 1 11 f0 f1 f2 … ff AFTER CACHE MISS
v t data
0xf2 = 11 11 0010 (tag=11, set=11, offset=0010)

## Slide 20: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0 0
S1 0
S2 1 11 e0 … ec ed ee ef CACHE MISS
S3 1 11 f0 f1 … fe ff
v t data
0xac = 11 10 1100 (tag=11, set=10, offset=1100)

## Slide 21: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0 0
S1 0
S2 1 10 e0.. ec ed ee ef
S3 1 11 f0 f1 … f6 … fe ff CACHE HIT
v t data
0xf6 = 11 11 0110 tag=11, set=11, offset=0110

## Slide 22: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0 0
S1 0
S2 1 10 e0.. ec ed ee ef
S3 1 11 f0 f1 … f6 … fe ff CACHE MISS
v t data
0x38 = 00 11 1000 (tag = 00, set = 11, offset = 1000

## Slide 23: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0 0
S1 0
S2 1 10 e0.. ec ed ee ef
S3 1 00 30 31 … 38 … 3e 3f AFTER CACHE MISS
v t data
0x38 = 00 11 1000 (tag = 00, set = 11, offset = 1000

## Slide 24: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0 0
S1 0
S2 1 10 e0.. ec ed ee ef
S3 1 00 30 31 … 38 … 3e 3f CACHE HIT
v t data
0x37 = 00 11 0111 (tag = 00, set = 11, offset = 0111

## Slide 25: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0 0
S1 0
S2 1 10 e0.. ec ed ee ef
S3 1 00 30 31 … 38 … 3e 3f
v t data
0x52 = 01 01 0010 (tag = 01, set = 01, offset = 0010
CACHE MISS, because set s1 is empty

## Slide 26: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52, 0xff, 0x11, 0x88
S0 0
S1 1 01 50 51 52 … 5e 5f AFTER CACHE MISS
S2 1 10 e0.. ec ed ee ef
S3 1 00 30 31 … 38 … 3e 3f
v t data
0x52 = 01 01 0010 (tag = 01, set = 01, offset = 0010

## Slide 27: Continue problem with the following memory accesses:
0x00, 0x80, 0x7f, 0x25, 0x47
S0 0
S1 1 01 50 51 52 … 5e 5f
S2 1 10 e0.. ec ed ee ef
S3 1 00 30 31 … 38 … 3e 3f
v t data

## Slide 28: Why are caches organized as such?
c
S0 1 00 ‘h’ ‘e’ ‘l’ ‘l’ ‘o’ ‘\0’ …
S1 1 01 50 51 52 … 5e 5f
S2 1 10 e0.. ec ed ee ef
S3 1 00 30 31 … 38 … 3e 3f
v t data
char buf[16];
scanf(“%s”, buf);
If buf starts at address 0x0000, then

## Slide 29: Why are caches organized as such?
c
S0 0
S1 1 00 ‘d’ ‘i’ ‘p’ ‘a’ … ‘o’ ‘s’
S2 1 00 ‘p’ ‘h’ ‘a’ … ‘e’ ‘s’ ‘\0’
S3 0
v t data
char buf[32];
scanf(“%s”, buf);
// input is dipalmitoylpho00 ‘d’ ‘i’ ‘p’ ‘a’ … ‘o’ ‘s’
sphatidylcholines
If buf starts at address 0x10, then
If the set bits were first, then the two blocks
would collide

## Slide 30: Example: M x N matrix
int sum_row(int matrix[ ][N], int M, int row) {
int ans = 0;
int I;
for (i=0; i<N; i++)
ans += matrix[row][i];
return ans;
Cache miss rate? Assume that M,N >> block size (B)

## Slide 31: Example: M x N matrix
int sum_column(int matrix[ ][N], int M, int col) {
int ans = 0;
int I;
for (i=0; i<M; i++)
ans += matrix[M][i];
return ans;
Cache miss rate? Assume that M,N >> block size (B)

## Slide 32
Matrix multiplication (n x n matrix)
// ijk
for (i=0; i<n; i++)
for (j=0; j<n; j++) {
c[i][j] = 0;
for (k=0; k<n; k++)
c[i][j] += a[i][k] * b[k][j]; // miss rate?

## Slide 34
# sets
Fetch time
for cache
hits

## Slide 35: Set associative caching
In direct map caching, there is one line per set (line = v + tag + block)
In set associative caching, there is more than one line per set

## Slide 36: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0
v t data
0
0
S1
0
0
S2
0
0
S3
0
0

## Slide 37: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0
v t data
0
0
S1
0
0
S2
0
0
S3
1 11 f0 f1 f2 … fd fe ff
0

## Slide 38: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0
v t data
0
0
S1
0
0
S2
0 11 e0 e1 e2 … ec ed ee ef
0
S3
1 11 f0 f1 f2 … fd fe ff
0

## Slide 39: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52
S0
v t data
0
0
S1
0
0
S2
0 11 e0 e1 e2 … ec ed ee ef
0
S3
1 11 f0 f1 … f6 … fd fe ff
0

## Slide 40: Assume that M[x] = x for all values of x. Show the cache (initially empty) for the following sequence of address fetches
0xf2, 0xec, 0xf6, 0x38, 0x37, 0x52, 0xff, 0x11, 0x88
S0
v t data
0
0
S1
0
0
S2
0 11 e0 e1 e2 … ec ed ee ef
0
S3
1 11 f0 f1 … f6 … fd fe ff
1 00 30 31 … 38 … 3e 3f